## Slide 1: Chapter 10 AVR Timer Programming in Assembly and C The AVR Microcontroller and Embedded Systems: Using Assembly and C M. A. Mazidi
Dr. Seyyed Javad Seyyed Mahdavi

## Slide 2: Contents
Programming Timers 0, 1, and 2
Counter Programming
Programming Timers in C

## Slide 3: A General View of Counters and Timers

## Slide 4: Programming Timers 0, 1, and 2
In ATmega32, there are three timers:
  Timer0, Timer1, and Timer2.
  Timer0 and Timer2 are 8-bit, while Timer1 is 16-bit.
Basic registers of timers
  TCNTn (Timer/Counter register)
  TOVn (Timer Overflow flag)
  TCCRn (Timer Counter control register)
  OCRn (output compare register)
  OCFn (output compare match flag)
  All of the timer registers are byte-addressable I/O registers
TCNTn
TCCRn
TOVn
OCRn
=
OCFn

## Slide 5: Programming Timers 0, 1, and 2 Basic registers of timers
Basic registers of timers
  TCNTn (Timer/Counter register)
  TOVn (Timer Overflow flag)
  TCCRn (Timer Counter control register)
  OCRn (output compare register)
  OCFn (output compare match flag)

## Slide 6: Programming Timers 0, 1, and 2 Basic registers of timers
TIFR (Timer/counter Interrupt Flag Register) register

## Slide 7: Programming Timers 0, 1, and 2 Timers 0 Programming
TCCR0 (Timer/Counter Control Register) Register

## Slide 8: Programming Timers 0, 1, and 2 Timers 0 Programming
TCCR0 (Timer/Counter Control Register) Register

## Slide 9: Programming Timers 0, 1, and 2 Timers 0 Programming
TCCR0 (Timer/Counter Control Register) Register

## Slide 10: Programming Timers 0, 1, and 2 Timers 0 Programming

## Slide 11: Programming Timers 0, 1, and 2 Timers 0 Programming
Normal mode
  When it rolls over from 0xFF to 0x00, it sets high a flag bit called TOV0.
Steps:
  Load the TCNT0 register with the initial count value.
  Load the value into the TCCR0 register which starts the timer
  Keep monitoring the timer overflow flag (TOV0) to see if it is raised.
    Get out of the loop when TOV0 becomes high.
  Stop the timer by disconnecting the clock source (following Instructions:)
  Clear the TOV0 flag for the next round.
  Go back to Step 1 to load TCNT0 again.

## Slide 12: Programming Timers 0, 1, and 2 Timers 0 Programming

## Slide 13: Programming Timers 0, 1, and 2 Timers 0 Programming

## Slide 14: Programming Timers 0, 1, and 2 Timers 0 Programming

## Slide 15: Programming Timers 0, 1, and 2 Timers 0 Programming

## Slide 16: Programming Timers 0, 1, and 2 Timers 0 Programming

## Slide 17: Programming Timers 0, 1, and 2 Timers 0 Programming

## Slide 18: Programming Timers 0, 1, and 2 Timers 0 Programming
Maximum delay in normal mode without Prescalar

## Slide 19: Programming Timers 0, 1, and 2 Timers 0 Programming
Maximum delay in normal mode without Prescalar

## Slide 20: Programming Timers 0, 1, and 2 Timers 0 Programming
Maximum delay in normal mode without Prescalar

## Slide 21: Programming Timers 0, 1, and 2 Timers 0 Programming
Maximum delay in normal mode without Prescalar

## Slide 22: Programming Timers 0, 1, and 2 Timers 0 Programming
Clear Timer0 on compare match (CTC) mode programming

## Slide 23: Programming Timers 0, 1, and 2 Timers 0 Programming
Clear Timer0 on compare match (CTC) mode programming

## Slide 24: Programming Timers 0, 1, and 2 Timers 0 Programming
Clear Timer0 on compare match (CTC) mode programming

## Slide 25: Programming Timers 0, 1, and 2 Timers 2 Programming
Timer 0
CS02 CS01 CS00 Comment
0 0 0 Timer/Counter stopped
0 0 1 clk (No Prescaling)
0 1 0 clk / 8
0 1 1 clk / 64
1 0 0 clk / 256
1 0 1 clk / 1024
1 1 0 External clock (falling edge)
1 1 1 External clock (rising edge)
CS22 CS21 CS20 Comment
0 0 0 Timer/Counter stopped
0 0 1 clk (No Prescaling)
0 1 0 clk / 8
0 1 1 clk / 32
1 0 0 clk / 64
1 0 1 clk / 128
1 1 0 clk / 256
1 1 1 clk / 1024
Timer 2

## Slide 26: Programming Timers 0, 1, and 2 Timers 1 Programming
More complicated

## Slide 27: Counter Programming
For Timer 0
  when CS02:00 is 6 or 7,
  the TCNT0 counter counts up as pulses are fed from pin T0
For Timer 1
  when CS12:10 is 6 or 7, the clock pulse coming in from pin T1 makes the TCNT1 counter count up.
  6, the counter counts up on the negative (falling) edge.
  7, the counter counts up on the positive (rising) edge.
T0

## Slide 28: Counter Programming

## Slide 29: Counter Programming

## Slide 30: Programming Timers in C

## Slide 31: Programming Timers in C

## Slide 32: Programming Timers in C

## Slide 33: Problems