## Slide 1: Exercise #2

## Slide 2: RUNSPEC Section
Purpose:
  Create a RUNSPEC section from scratch.
Grid Dimensions - 24 x 25 x 12
Oil field - initially under-saturated.
Aquifer support suspected (you should use a Fetkovich aquifer).
Production from 1-January-1998.
5 producers; As many as 2 wells may be drilled in the future.
Request unified input and output files.
Use field units.

## Slide 3: GRID Section
Purpose:
  Specify reservoir geometry and basic rock properties. Data:
    Porosity and Permeability obtained from wells drilled throughout reservoir (table).
    Kz/Kx = 0.1
    Corner point geometry created previously in Petrel - Field.GRDECL
Request the following output:
  EGRID and INIT file
  Transmissibility and NNCs to PRT file

## Slide 4: PROPS and REGIONS Sections
Purpose:
  Supply and verify reservoir fluid PVT properties.
  Supply and verify relative permeability & capillary pressure data.
  Define distinct reservoir regions.
Relevant Data:
Surface Densities (Ib/ft3) - Oil 42.28; Water 62.43; Gas 0.0971.
Bw is 1.013 rb/stb at 3118 psia, μw is 0.4 cP and Cw 2.74x10-6 (psi)-1
Cr is 2.8x10-6 (psia)-1 at Pi
PVT and Saturation tables are supplied in 'PROPS_Data.xls' spreadsheet

## Slide 5: Initialization
Purpose:
  Supply initial conditions & define the aquifer
Data:
  Bubble point pressure is 1062.2 psia, GOR is 973 scf/stb.
  Oil-Water Contact: 8200 ft (free water level)
  Pressure: 3035.7 psia at 7000 ft
  Aquifer support: Volume 1x107 stb; PI 5 bbl/day/psi

## Slide 6: History Match
Purpose:
  Adjust properties to match measured production.
Well data:
  All wells have an internal diameter of 0.625 feet and skin of 7.5.
  Well production history is in HIST.SCH file.

## Slide 7: History Match (cont.)
Process:
Complete the field dataset by supplying well definitions and production history.
Run sensitivities on
  Fault transmissibility
  Aquifer volume and deliverability (Productivity Index)
Complete history match for pressure.
(Optional) Use oil rate control and match water production.

## Slide 8: Recovery Optimization
Purpose:
  Create restart run.
  Use various group production / injection controls to optimize recovery.
Process:
  Create restart run with current production rates.
  Compare with group production control.
  Compare constant water injection to voidage replacement and production balancing.
  Investigate gas reinjection.